## Slide 1
Exploratory Data Analysis
Preparing Soil Moisture Forecasts for Automated Irrigation
Data Wrangling · Feature Engineering · LSTM Readiness

## Slide 2
Project Context
Field Study at a Glance
We wired each randomized corn plot with soil moisture probes (6/18/30 cm), canopy temperature sensors, and a weather tower feeding a CR1000X datalogger.
Growers revisit irrigation every four days. We want a four-day VWC lookahead so they can act before stress sets in.
What makes this tricky? Three months of data but dozens of plots. The model has to mix short timelines with cross-field variety so one brain serves everyone.

## Slide 3
Why Predict VWC Four Days Ahead?
Growers rely on the Soil Water Stress Index (SWSI) to plan irrigation. We forecast volumetric water content (VWC) four days ahead, then derive SWSI so agronomists can act before stress appears.
Accurate VWC forecasts keep the SWSI ratio inside the safe band for each plot.

## Slide 4
Sensor to Cloud Data Pipeline
Insert the field instrumentation diagram here: soil moisture probes at 6/18/30 cm, canopy temperature sensors, CR1000X logger, LoRa gateway, and the cloud database feeding this analysis.
IMAGE PLACEHOLDER — Full pipeline diagram
Sensors → Datalogger → Gateway → Wireless backhaul → Cloud data lake

## Slide 5
What Did We Measure?
Every plot streams an hourly record from late July through September 2023. We ingested roughly 2,000 timestamps per sensor channel across seven RCBD blocks.
Sensor Stack
Soil moisture (6/18/30 cm), canopy temperature, weather tower, irrigation pulse totals.
Spatial Scale
Plots 2003–2015 share the crop but differ in irrigation strategy; the model must span them all.
Timeframe
Hourly readings roll up to daily averages, aligned with the four-day irrigation cycle.

## Slide 6
Native Channels Logged Each Hour
Why it matters
The notebook pulls these channels straight from process_data_for_plot and passes them to every downstream transform.
If we ever disable a sensor, we edit the table and the code together to keep the data wrangling honest.
TABLE PLACEHOLDER — Native sensor channels

## Slide 7
Engineered Features Fed to the Model
Feature recipe
The notebook adds spike flags, smoothed trends, derivatives, time-since-water counters, and log-scaled precipitation totals—exactly the columns listed here.
If a feature ever drops from this table, it has dropped from the code too.
TABLE PLACEHOLDER — Engineered feature set

## Slide 8
First Pain Point: Missing Hours Everywhere
Cables get chewed, solar panels get cloudy, and irrigation events knock radios offline. In the raw export the notebook loads, these outages show up as NaNs sprinkled across every channel.
What we learned from the raw export
Soil probes can go dark for days while the weather tower keeps logging.
Power loss knocks out every channel, which is why we trim the dataset ends in code.
Each plot recovers on its own schedule, so we avoid borrowing from neighbours.
Next up is the gap profile by column so we can target the worst offenders.

## Slide 9
Gap Profile by Sensor Channel
Missing hours pile up fastest in the soil moisture depths, confirming the need for careful interpolation.

## Slide 10
Cleaning Before Feature Work
Before we engineer any features the notebook runs four quick steps (all inside process_data_for_plot) to line up every plot and prevent duplicate readings from skewing the daily averages.
1. Trim outages
Clip the dataset ends until every column has data.
2. Drop duplicates
Remove timestamps replayed after logger reboots.
3. Set index
Sort by TIMESTAMP so resampling and windowing stay stable.
4. Resample daily
Aggregate hourly readings to daily means for the four-day horizon.

## Slide 11
Gap Filling with PCHIP
We interpolate daily VWC gaps with SciPy’s Piecewise Cubic Hermite (PCHIP) spline. It keeps the curve monotonic between known points so dry-down periods stay smooth.
Hermite basis functions blend neighbouring values and slopes so the fill extends the real dry-down pattern.
Reality check: right now we fill every day, even the wet ones. That flattens the irrigation spikes. Masking days with ≥5 mm of water before filling would keep those jumps intact.

## Slide 12
PCHIP Fills VWC Gaps Smoothly
Daily averages for plot 2003 after interpolation. Because we currently fill every day, irrigation spikes get softened—masking wet days before PCHIP would preserve those jumps.

## Slide 13
Smoothing & Daily Change Features
After interpolation we smooth each depth with a 20-day Savitzky–Golay filter so the signal reflects crop-scale trends instead of probe jitter.
ΔVWC captures how quickly the profile is drying or being refilled.
Positive ΔVWC flags irrigation or rain recharge events.
Negative ΔVWC matches evapotranspiration drawdown between irrigations.

## Slide 14
Savitzky–Golay Reveals the Trend
Smoothed curves (solid) follow the interpolated series (dotted) while stripping sensor chatter. These become the basis for derivative features.

## Slide 15
ΔVWC Highlights Recharge Events
After smoothing, the notebook takes a simple first difference to see how fast moisture is changing. Positive spikes flag irrigation or rain; negative runs trace evapotranspiration between events. If the signal ever gets noisy, we could switch to centred or multi-day slopes.

## Slide 16
Flagging Spikes for Irrigation Awareness
Sudden jumps in VWC usually mean we irrigated, injected fertilizer, or caught a thunderstorm. The model needs to recognize these events explicitly.
Spike up: the code marks a recharge when VWC today is 1.15× yesterday.
Spike down: a 15% drop flags drainage or unplugged probes.
Flags are computed per depth so shallow and deep responses stay distinct.
15% came from the 2023‑08‑03 fertigation run. If we see missed events, we can tune the multiplier in process_data_for_plot.

## Slide 17
Spike Flags by Depth · Plot 2014
Each depth responds differently. The binary flags align with the ΔVWC spikes we saw earlier, giving the model a crisp indicator of irrigation timing.

## Slide 18
Temporal Features & Safe Scaling
The notebook tracks how long the soil has been drying (time_since_last_precip), how much water arrived in the past week, and a log-transformed irrigation signal so micro-pulses survive scaling. The counter resets whenever precip_irrig tops 0.2 in (≈5 mm), and the seven-day sum shows how much water remains in the soil.
A 30% buffer keeps scaled features inside [0,1] even when validation plots see more water than training.
If we ever hit the bounds, we can widen the buffer or fit scalers per treatment block.

## Slide 19
Days Since Water — Plot 2014
The code resets the counter whenever precip_irrig tops 0.2 in (≈5 mm), so the stair steps match the four-day irrigation rhythm.

## Slide 20
Water Supply Features After Scaling
Buffered MinMax scaling keeps the transformed precipitation signals inside [0,1] even when unseen storms arrive.

## Slide 21
How We Frame the Forecast
For every plot the notebook takes a seven-day window of scaled features and asks the LSTM to predict VWC four days ahead. That window length mirrors the grower’s four-day irrigation cadence—enough history to see the last watering and the dry-down that followed.
Right now we slide the window forward one day at a time, so neighbouring sequences overlap. That keeps the training set large but can blur independent decisions. If we want strictly non-overlapping forecasts we could stride by four days instead. Each window covers seven days of features and produces four future days of VWC for all three depths.

## Slide 22
LSTM Stack & Training Setup
The notebook builds a four-layer LSTM stack (512 → 256 → 128 → 64 units) with batch normalisation and dropout after each layer, then reshapes a dense layer into four forecast days × three depths.
Optimizer: Adam starting at 0.001 with exponential decay after epoch 15.
Loss: Mean Squared Error across the entire four-day horizon.
TimeSeriesSplit (5 folds) keeps each plot’s chronology intact while sharing weights across plots.
Batch size 128, patience 200 to let training settle without overfitting.
Predictions are inverse-transformed with the stored MinMax scalers and means so evaluation happens in %VWC. If we see values pinning at 0 or 1 we can widen the 30% buffer.

## Slide 23
Performance & Open Questions
Cross-plot RMSE sits around 0.025 m³/m³ across the four-day horizon. The model tracks seasonal dry-down well but barely reacts when we inject extra irrigation into the inputs.
Temporal features and spike flags keep predictions aligned in dry periods.
Buffered scaling prevents values from clipping when validation plots get more rain.
The irrigation signal needs work—loss weighting or water balance features would help the network respect those pulses.