## Slide 1
Exploratory Data Analysis
LSTM-Based Soil Moisture Prediction for Automated Irrigation Scheduling
Data Wrangling and Feature Engineering Workflow

## Slide 2
Project Context
Automated Irrigation Scheduling Study
Research goal: Develop data-driven irrigation scheduling system for corn cultivation
Multi-sensor data collection: soil moisture, canopy temperature, weather data
3-month study period with hourly measurements
Multiple plot ranges (spatially distributed data)
Fixed 4-day irrigation cycle constraint
Core Challenge: How to leverage limited temporal data (3 months) with high spatial resolution (multiple plots) to train time series prediction models?

## Slide 3
Problem Statement
Predicting Volumetric Water Content (VWC)
Goal: Predict soil moisture 4 days ahead to prevent water stress
Soil Water Stress Index (SWSI)
SWSI = 1 - (θ / θFC)
θ = current VWC, θFC = field capacity
Why predict VWC?
Direct sensor measurements
Can derive SWSI from VWC
Preempt stress over 4-day cycle

## Slide 4
Data Collection Pipeline
IMAGE: Complete Data Flow Diagram
Sensors → Data Logger → Gateway → Wireless → Cloud
Full pipeline showing VWC sensors, canopy temperature sensors, data logger, wireless gateway, and cloud storage

## Slide 5
Dataset Summary
3
Months
~90
Days
Hourly
Sampling
Multiple
Plot Ranges
Key Characteristics
Corn hybrid DK-672 grown in RCBD plots 2003–2015 with LoRa telemetry
Hourly sensor pulls from 2023-07-20 → 2023-09-30 (≈2,000 rows per channel)
Synchronized canopy temp, VWC_06/18/30, weather, and irrigation counters
Frequent outages: chewed sensor leads + cloudy weeks → multi-day gaps

## Slide 6
Native Data Features
Raw Data Columns Collected
TABLE: All Native Features
TIMESTAMP, VWC_06/18/30, canopy_temp, Ta/RH/Solar towers, wind, rain, irrigation pulse totals pulled directly from CR1000X logger
Feature | Description | Units
Ta_2m_Avg | Air temperature at 2m | °C
RH_2m_Avg | Relative humidity at 2m | %
Solar_2m_Avg | Solar radiation at 2m | W/m²
WndAveSpd_3m | Wind speed at 3m | m/s
Rain_1m_Tot | Rainfall total at 1m | mm
VWC_06/18/30 | Volumetric water content (depths) | %
canopy_temp | Canopy temperature | °C
irrigation | Irrigation amount | mm
precip_irrig | Combined precip + irrigation | mm

## Slide 7
Engineered Features
Features Created During Data Wrangling
TABLE: Engineered Features
Binary spike flags (±15% day-over-day), time-since-precip counters, 7-day precip/irrig sums, Savitzky-Golay smoothed VWC traces, sin/cos encodings for hour + DOY
Feature | Description | Purpose
VWC_*_spike_up | 15% increase detection | Capture irrigation/rain events
VWC_*_spike_down | 15% decrease detection | Detect rapid drainage
time_since_last_precip | Days since last rain event | Temporal drought indicator
precip_cumulative_7day | 7-day rolling sum | Water supply over window
VWC_*_smoothed | Savitzky-Golay filtered | Noise reduction
VWC_*_deriv | Rate of change | Capture dynamics
precip_irrig_log | Log-transformed precip | Handle skewed distribution
Cyclic time encoding | Sin/cos of hour, day, DOW | Capture temporal patterns

## Slide 8
Raw VWC Data - The Challenge
Volumetric Water Content with Data Gaps
IMAGE: Raw VWC Time Series Plot
Shows VWC_06, VWC_18, VWC_30 over time
Highlighting multiple data gaps due to:
Pest damage to sensor wires
Power outages (insufficient solar)
Real-world field conditions

## Slide 9
Domain Knowledge is Critical
"Field intuition converts logger noise into features – we have to encode irrigation timing, infiltration lag, and chewed-wire outages."
Warden silt loam shows 2–6 hour infiltration lag before VWC sensors spike
Fertigation crew logs night-time pulses → mark windows to avoid interpolation
CR1000X stations lose power after 3 cloudy days; trim those dead zones first
RCBD layout demands plot-aware scaling so LSTM learns cross-plot dynamics

## Slide 10
Basic Data Cleaning
Essential Preprocessing Steps
1. trim_start_end_nans(df)
Walks each column to find first/last valid timestamp so storm outages are clipped
2. drop_duplicates()
CR1000X occasionally double-logs hourly rows after reboot – eliminate duplicates
3. set_index('TIMESTAMP')
Indexing enables resample windows and sliding-window sequence generation
4. resample('D').mean()
Daily aggregation tested vs. hourly – no perf loss but smoother VWC trajectories
Code Example
# Cleaning pipeline anchored in notebook
df = trim_start_end_nans(raw_df)
df = (df.drop_duplicates()
.set_index('TIMESTAMP')
.sort_index()
.resample("D").mean())

## Slide 11
Interpolating Missing Values
PCHIP (Piecewise Cubic Hermite Interpolating Polynomial)
H(t) = y_k h_1(t) + y_{k+1} h_2(t) + h_k m_k h_3(t) + h_k m_{k+1} h_4(t)
Why PCHIP? SciPy's PchipInterpolator keeps VWC curves monotone during dry-down and prevents Gibbs overshoot
Critical Constraint: Only interpolate during periods with NO rainfall
Rain/fertigation spikes VWC ≈0.2 within six hours
Mask those windows so interpolation never bridges forced spikes
Dry stretches: ET pulls ≈0.005 per day (slow slope)
Carry latest decline rate forward to span gaps

## Slide 12
Spike Detection
Detecting VWC Spikes (Irrigation & Rainfall Events)
Purpose: Capture sudden water injection events as binary features
Spike Up: VWC_06/18/30 rising >1.15× day-1 flagged fertigation and rain pulses
Spike Down: >15% drop reveals drainage events or unplugged probes
Threshold tuned from 2023-08-03 fertigation run (0.22 → 0.28 m³/m³)
Implementation Sketch
for col in VWC_COLUMNS:
up = df[col] > df[col].shift(1) * 1.15
down = df[col] < df[col].shift(1) * 0.85
df[f"{col}_spike_up"] = up.astype(int)
df[f"{col}_spike_down"] = down.astype(int)

## Slide 13
Time Since Precipitation
Capturing Temporal Distance from Water Events
Rationale: Time since last significant input reveals how quickly soil moisture should decay
Two thresholds tracked:
Days since >0.2 in precip (5 mm irrigation setpoint)
Days since half-max storm (0.5 × seasonal peak)
Feature Engineering Snippet
mask = (df['precip_irrig'] > 0.2).astype(int)
df['time_since_last_precip'] = (
mask.cumsum() - mask.replace(0, None).cumsum()
).fillna(0)
df['precip_irrig_cum_7day'] = df['precip_irrig'].rolling(7).sum()

## Slide 14
Savitzky-Golay Filter
Smoothing VWC Data
Purpose: Remove high-frequency noise while preserving irrigation spikes
savgol_filter(x, window=20, polyorder=4, deriv=0)
Window: 20-day kernel filters 30 cm probe chatter yet keeps seasonal drift
Order: Degree 4 preserves irrigation spikes lasting 2–3 days
Derivative: 0 → smooth VWC_06/18/30 prior to differencing
Implementation Sketch
for col in target_columns:
df[col] = savgol_filter(
df[col], window_length=20, polyorder=4, deriv=0
)

## Slide 15
Data Transformations
Preparing Data for Neural Network
1. Mean Subtraction
Store μ for VWC_06/18/30 per plot, subtract so LSTM sees anomalies not absolute moisture
2. Derivative Features
Add ΔVWC columns via diff() to encode daily depletion velocity after irrigation
3. MinMax Scaling
Scale channels to [0,1] with 30% buffer so storms and injections stay in range
4. Log Transform
Use log(precip_irrig + 1) to convert skewed irrigation pulses into learnable increments

## Slide 16
Scaling: MinMax with Buffer
Why Scaling Matters
LSTM trains faster when VWC_06/18/30, canopy_temp, precip share [0,1] scale
Buffered scaling avoids exploding gradients when a block floods
Cross-plot mixing needs consistent ranges despite differing soil textures
Keeps irrigation pulses comparable with weather covariates
Buffer Rationale
30% buffer keeps injected irrigation scenarios and rare storms within scaler bounds
MinMax Formula
range = max - min
buffer = 0.3 × range
scaled = (x - (min - buffer)) / ((max + buffer) - (min - buffer))
buffered_min = min_val - buffer # per column, per plot
buffered_max = max_val + buffer
scaled = (data - buffered_min) / (buffered_max - buffered_min)